 Droplet Confined in parallel plate
Fig:Evaporation of squeezed water droplets between two parallel hydrophobic/superhydrophobic surfaces,Xukun He

---
Physics Modules used
- Laminar Flow
  - The Laminar Flow (spf) interface is used to compute the velocity and pressure fields for the flow of a single-phase fluid in the laminar flow regime
  - Wetted wall to pin the droplet at desirable CA
- Level Set
  - The level set method is a technique to represent moving interfaces or boundaries using a fixed mesh.
  - Allows for incorporation of mass flux at interface

---
Results
Studing the system at constant contact angle regime at various contact angles
At pi/6:
t=0
t=10

---
At pi/3:
t=0
t=10
At 3pi/2:
t=0
t=10
t=20

---
Results
- Splitting of droplet at exterme contact angle, using finer mesh might prevent this
- Droplet settle at expected position in the nominal cases
- Gravity is neglected in the study, so the assymetry in the 3pi/2 case is unexpected

---
To do
- Work on droplet splitting
- Velocity flow inside the droplet, could be tracked precisely using Particle tracking method
- Incorporate the mass flux at the interface and study the evolution of the droplet at various volume
Fig 9:Numerical simulation of droplet evaporation between two
circular plates† Hangjin Ban and Gihun Son*